## Slide 1: Interworking between Web of Things and t2trg/CoRE
Kunihiko Toumura
Hitachi, Ltd.
6 November 2019

## Slide 2: Working Items in new WoT-WG charter and t2trg/CoRE activity
For new WG charter work items, WG starts collecting use cases and extracting requirements. The workshop/hackathon is a good opportunity to investigate how to interwork with t2trg/CoRE, as a case study for the work items.
Current Charter Draft:
  http://w3c.github.io/wot/charters/wot-wg-charter-draft-2019.html
2.5 Complex Interactions
  How to describe a CoRAL-based device?
2.6 Discovery, 2.8 Onboarding
  We can use a CoRE-RD framework for one of discovery mechanism to retrieve WoT Thing Description and Thing.
2.10 Security Schemes
  Use of OSCORE, ACE etc.
2.12 Protocol Vocabulary and Bindings, 2.13 Observe Defaults
  Use of CoAP Observe

## Slide 3: Complex Interactions (1/2): Differences
(Current) WoT Thing Description contains all interactions that a thing provides, regardless of current state of the Thing.
CoRE/CoRAL takes pure HATEOAS approach, i.e. an CoRAL document may contain interactions that are meaningful in current state.
Thing
Consumer
Thing
Consumer
Retrieve TD from somewhere
Consume TD
Select an interaction and make an HTTP request
Thing returns a requested property
or a result of the action
Select an interaction and make an HTTP request
Thing returns a requested property
or a result of the action
Retrieve an entry point URI from somewhere
GET request on entry point URI
Returns CoRAL document (1) that contains properties(embedded representation), or link/form for next action
Select an interaction from recent CoRAL document(1)
And make CoAP request
Returns another CoRAL document (2)
Select an interaction from CoRAL document (2)
And make CoAP request
Returns yet another CoRAL document (3)
State 1
State 2
State 3
state
Triggers
state
transition
state
Triggers
state
transition
state
State machine of the Thing
State?
State machine of the Thing

## Slide 4: Complex Interactions (2/2): Possible approach
How to interact pure RESTful-style thing from WoT consumer?
  Static TD: Introduce a concept of “State Machine” to Thing Description
    TD describes all possible interactions of the Things.
    Designate feasible interactions of each state using state machine.
    Interaction with a Thing triggers a state transition in Consumer’s state machine.
  Dynamic TD: Consumer updates its internal Thing Description dynamically, based on a response from the Thing
    Based on recent Thing Description, an application select a feasible interaction.

## Slide 5: Discovery
CoRE proposes several discovery and directory mecanisms.
  Discover Things by CoAP multicast on well-known URI (/.well-known/core)
    Discovery of Resource Directory is similar approach (i.e. use “/.well-known/core/?rt=core.rd*”)
  Moreover, IPv6 Authoritative Border Router Option, DHCP, DNS-SRV can be used for discovery of Things and RDs
Can we use these mechanism to retrieve Thing Description?
(This work does not intend to propose that this is THE discovery mechanism of Web of Things. Just a case study.)

## Slide 6: Ideas for IETF Hackathon
Implementing WoT TD discovery based on CoRE-RD.
  Discover Resource Directory based on multicast
    coap://("all CoRE resource directories" address)/.well-known/core?rt=core.rd*
  Register TD to CoRE-RD
    POST coap://rd.example.com/rd?ep=(Thing-ID)
    Content-Format: application/td+json (Content-format ID is t.b.d., in the 256-9999 range)
  Retrieve TD from CoRE-RD
    GET coap://rd.example.com/rd-lookup?rt=MyLampThing
    Accept: application/td+json
  Using retrieved TD, interact with the Thing (e.g. generate Node-RED node, etc.)
    Interaction protocol: HTTP(S), CoAP(S)